## Slide 1
Sensorless Load Estimation Using Motor Slip
on a Low-Cost VFD-Driven Induction Motor
Progress Update
David Salisbury
AEEE-6850 Capstone Project — UNC Charlotte
October 2026
1

## Slide 2
Design Requirements
Project goal
Estimate an unknown mechanical load on a VFD-driven induction motor using motor slip — no added torque sensor
Build a low-cost, embedded data-acquisition system around the existing VFD and motor
Compare the slip-based load estimate against a current-based estimate
Provide a standalone keypad + display interface so the rig can be operated without a laptop
Course requirements (AEEE-6850 syllabus)
Builds on Summer 2026 independent study (VFD + induction motor speed control)
Formal presentation to faculty mentor and at least one other AEES faculty member
A professional, conference-formatted paper documenting the project and results (IEEE / ASME style)
2

## Slide 3
Test Rig Overview
VFD: AutomationDirect DURApulse GS23-21P0 (scalar V/Hz)
Motor: Lucas-Nülle SE2673-1K7, 0.37 kW, 4-pole induction motor
Controller: STM32 Nucleo-F401RE — reads VFD frequency/current over RS-485 Modbus RTU
Load path: hoist drum + cable, known weights hung on a hook
Shaft speed reference: Lucas-Nülle ActiveServo (SB2663-6U), read by eye
Insert photo of test rig
3

## Slide 4
PC Logger — Live Data
Each logged row: time, output frequency, synchronous speed, shaft RPM, slip, output current, known load, test ID
Every motor run is saved automatically to its own file; a summary file collects one line per run
The logger prompts for the shaft RPM reading after each run
Insert screenshot of logger window
4

## Slide 5
Status — Completed
VFD configured and verified for potentiometer speed control (VFDCHECK: 8/8 settings pass)
RS-485 / Modbus RTU communication to the VFD confirmed (output frequency + output current registers)
STM32 firmware: logs frequency, current, synchronous speed, and slip every 250 ms; TEST/STOP test sessions with steady-state averaging
PC logger (Python): automatically saves every motor run and prompts for the shaft RPM reading
No-load baseline data collected at four speeds (1.39, 2.44, 4.85, 6.36 Hz); 6.36 Hz selected as the fixed calibration speed
Baseline results documented in a written report, traceable back to every source data file
5

## Slide 6
Status — Not Yet Complete
Weighted-load calibration runs — the data needed to actually build the predictive model
Keypad + HMI integration on the controller (data entry, predicted load/speed display)
Predictive model: fit and validate slip-to-load and current-to-load estimates
Short conference-formatted paper
Final presentation to faculty
6

## Slide 7
Baseline Results So Far (No Load)
One up and one down run per speed; slip = (sync RPM − shaft RPM) / sync RPM.
Freq (Hz) | Sync RPM | Up slip | Down slip | Up current (A) | Down current (A)
1.39 | 41.8 | 0.270 | 0.091 | 0.476 | 0.486
2.44 | 73.3 | 0.182 | 0.052 | 0.466 | 0.434
4.85 | 145.4 | 0.054 | 0.030 | 0.814 | —*
6.36 | 190.7 | 0.056 | 0.025 | 0.704 | 0.651
6.36 Hz chosen as the fixed calibration speed — repeatable results, good RPM-display resolution, short run time
Slip is strongly direction-dependent (lifting vs. lowering); current is a much weaker signal than slip
Insert slip-vs-frequency plot
* 4.85 Hz down: only one full run was logged that session (the up run); the down RPM was noted by eye with no matching logged run, so no current reading exists for it.
7

## Slide 8
What's Left
Run weighted calibration tests at 6.36 Hz (known loads, up and down, several repeats per weight) to build the slip-to-load and current-to-load models
Add a keypad and HMI display to the controller:
Keypad — enter test data (load, RPM) directly at the rig
HMI display — show the predicted load and speed in real time
Fit and validate the predictive model against held-out data
Write the short conference-formatted paper
Prepare and deliver the final presentation
8

## Slide 9
Timeline
Last day of classes: December 2
Dates | Milestone
Oct 7 – Oct 17 | Weighted-load calibration tests at 6.36 Hz (known loads, up/down, repeats)
Oct 17 – Oct 31 | Keypad + HMI integration (data entry, predicted load/speed display)
Oct 31 – Nov 14 | Fit and validate the predictive model (slip-to-load, current-to-load)
Nov 14 – Nov 21 | Write the short conference-formatted paper
Nov 21 – Nov 30 | Finalize paper; prepare final presentation
Dec 2 | Final presentation and paper submission (last day of classes)
9

## Slide 10
Questions?
10