## Slide 1
Sensorless Load Estimation Using Motor Slip
on a Low-Cost VFD-Driven Induction Motor
David Salisbury
Department of Mechanical Engineering and Engineering Science
William States Lee College of Engineering — University of North Carolina at Charlotte

## Slide 2: Agenda
Motivation
Why sensorless load estimation
System Architecture
VFD, controller, HMI, and the signal path
Modbus / RS-485 Interface
Reading the drive's own telemetry
Slip Methodology
Computing load proxy signals
Hardware Validation
What has been confirmed so far
Next Steps
Calibration and future work

## Slide 3: The Problem: Load Sensing Is Expensive to Retrofit
Knowing instantaneous mechanical load helps detect faults, verify setpoints, and characterize a system.
Conventional solution: a dedicated torque transducer or load cell.
These are costly relative to the motor itself and require shaft or structural modification.
Rarely justified outside of dedicated test stands — especially in teaching labs or small industrial drives.
Our Approach
Use signals the VFD already measures — no added sensor, no shaft modification.

## Slide 4: Two Sensorless Signals, Already Available at the Drive
Motor Slip
Rotor speed falls below synchronous speed under load. The gap — slip — grows with mechanical load torque.
Output Current
Stator current rises to produce the additional electromagnetic torque a higher load demands.
Both increase with load, through independent physical mechanisms — a built-in cross-check.

## Slide 5: System Signal Path
HMI
LCD + Keypad
↔
STM32F401RE
Modbus Master
↔
RS-485
Modbus RTU
↔
VFD
GS23-21P0
↔
Induction Motor
+ Load
The microcontroller polls the VFD for telemetry, serves a standalone HMI, and streams a CSV log over USB.

## Slide 6: Hardware Platform
DURApulse GS23-21P0 VFD
1 HP class drive, single-phase in / 3-phase out, driving a 4-pole induction motor
STM32 Nucleo-F401RE
Bare HAL/LL C firmware — deterministic UART timing, no Arduino abstraction layer
MAX485 RS-485 Transceiver
Half-duplex Modbus RTU link, single GPIO drives DE/RE direction control
16×2 LCD + 4×4 Keypad
Standalone operator interface — no laptop tethered to the rig

## Slide 7: Modbus RTU over RS-485
Function code 0x03 — Read Holding Registers
9600 baud, 8 data bits, no parity, 2 stop bits (8N2)
Drive's P09.04 parameter has no 8N1 option for RTU — framing mismatch means zero response
DE/RE direction control on a single GPIO, asserted only while transmitting
Register | Address | Scale
Output Frequency | 0x2103 | raw ÷ 100 (Hz)
Output Current | 0x2104 | raw ÷ 100 (A)
Both registers validated end-to-end on real hardware against GSoft2's own live monitor.

## Slide 8
Lesson Learned
Trust the Hardware, Not the Manual
÷10
manual-text assumption — wrong by 10×
÷100
confirmed on real hardware: raw 69 = 0.69 A — matched GSoft2 exactly
Current register scale was assumed from a summarized manual, then corrected by cross-checking a live reading against the vendor's own configuration software.

## Slide 9: Standalone Human-Machine Interface
16×2 character LCD (PCF8574 I²C backpack) + 4×4 matrix keypad
Top line: live output frequency and current
Bottom line: most recently entered RPM / load
A / B / C / D select Load, RPM, Frequency, or Current
Digits + * (decimal) build a value, # confirms
Mirrors the serial commands exactly — same CSV log either way
Operates without a laptop tethered to the rig
Written and integrated into the same codebase as the validated Modbus path; not yet exercised on the assembled LCD/keypad hardware.

## Slide 10: Computing Slip as a Load Proxy
Synchronous speed: Ns = 120 f / P
Slip: s = (Ns − Nr) / Ns
f = VFD output frequency, read over Modbus
Nr = shaft speed, from an independent reference during data collection
Four-pole motor (P = 4) → Ns = 30f
Slip increases approximately monotonically with load torque — the physical basis for using it as a proxy

## Slide 11: Planned Calibration Procedure
Apply a known load via pulley + custom spool and a crane-scale reference
Log slip and current once the drive settles at each operating point
No-load baseline sweep establishes the unloaded slip-vs-frequency curve
Fit load-vs-slip and load-vs-current regressions, evaluate on held-out points
Point | Commanded f (Hz) | Load Condition
1 | 10 | No load (baseline)
2 | 10 | Loaded
3 | 20 | No load (baseline)
4 | 20 | Loaded
5 | 30 | No load (baseline)
6 | 30 | Loaded

## Slide 12: Hardware Validation Results To Date
9.95–16.60 Hz
Output frequency range logged over Modbus, cross-checked against GSoft2
0.67–0.70 A
Output current at light/no load, matching GSoft2's live monitor
1.4%
Computed slip at 491 RPM / 16.60 Hz — physically consistent with a lightly loaded motor
Full load-sweep calibration has not yet been executed — these results validate the measurement chain itself as the precondition for that calibration to be meaningful.

## Slide 13: Limitations to Account for in Calibration
Drive-reported frequency
Commanded/estimated, not a direct rotor-flux measurement
Register resolution
0.01 Hz / 0.01 A bounds sensitivity near no-load conditions
Rotor resistance drift
Winding temperature shifts the slip-vs-torque relationship
Mechanical fixture losses
Pulley/spool friction adds unmodeled offset and scatter

## Slide 14
Conclusion & Next Steps
Modbus RTU communication, register scaling, and the slip-computation pipeline have been validated end-to-end on real hardware.
Execute the full load-sweep calibration across the drive's operating range
Fit and validate slip-based and current-based load regressions
Bring up and test the HMI firmware on the assembled LCD/keypad hardware
Extend to networked logging / a live dashboard; repeat on other VFD/motor pairs

## Slide 15: Thank You
Questions?